## Slide 1: Networking Introduction

## Slide 2: OSI vs TCP/IP
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application
Transport
Internet
Network Access
Application Protocols
Ports UDP TCP
IP
MAC
OSI
TCP/IP

## Slide 3: Encapsulation Decapsulation
Application
Transport
Internet
Network Access
01A3041132AB
01A30411ED14
192.168.10.12
192.168.10.15
49791
80
DATA
Application
Transport
Internet
Network Access
192.168.10.12
192.168.10.15
49791
80
DATA
49791
80
DATA
DATA
01A3041132AB
01A30411ED14
192.168.10.12
192.168.10.15
49791
80
DATA
192.168.10.12
192.168.10.15
49791
80
DATA
49791
80
DATA
DATA
192.168.10.12
01A3041132AB
192.168.10.15
01A30411ED14
Ports
TCP or UDP
IP Addresses
MAC Addresses

## Slide 4: Addressing
Physical – Media Access Control (MAC Address) of NIC
Logical – IP Address of NIC
Network Services – Port numbers

## Slide 5: Physical Address (MAC Address)
MAC Address - basically made up of two parts
  Vendor Address
  Random Address
013E1FBB23A1
  013E1FBB23A1 – First part is the Vendor Address
  013E1FBB23A1 – Last part is the Random Address
FFFFFFFFFFFF
  Special MAC address for Broadcasts
This is how computers communicate with each other NIC to NIC

## Slide 6: Logical Addresses (IP)
IP addresses can be used to:
  Provide a unique address for a host
  Provide a way to group hosts on a subnet
  Facilitate the transmission of network packets (data) between
    Local hosts (on the same subnet)
    Remote hosts (on different subnets separated by routers)
  Provide private addresses
  Provide public addresses
  Allow private addresses to be translated to public and back again

## Slide 7: IP Addresses and Binary
131.107.1.4
  Dotted decimal notation
  Each decimal number represents an octet (8 binary digits)
  0 = 00000000 (Minimum value)
  255 = 11111111 (Maximum value)
131 = 10000011
107 = 01101011
1 = 00000001
4 = 00000100
131.107.1.4 = 10000011 01101011 00000001 00000100

## Slide 8: Binary
Consists of 0 or 1 (off / on)
Counting in binary:
  00000000 bin = 0 dec
  00000001 bin = 1 dec
  00000010 bin = 2 dec
  00000011 bin = 3 dec
  00000100 bin = 4 dec
  00000101 bin = 5 Dec
  ….
  11111111 bin = 255 dec

## Slide 9: For each 1 in binary add the corresponding decimal values:
Binary to Decimal conversion |  |  |  |  |  |  | 
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
11111111 bin => 128+64+32+16+8+4+2+1 = 255 dec |  |  |  |  |  |  | 
Binary to Decimal conversion |  |  |  |  |  |  | 
1 | 0 | 1 | 0 | 1 | 0 | 1 | 1
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
10101011 bin => 128+32+8+2+1 = 171 dec |  |  |  |  |  |  | 
Binary to Decimal conversion |  |  |  |  |  |  | 
0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
10010 bin => 16+2 = 18 dec |  |  |  |  |  |  | 

## Slide 10: IP Address (Network vs Host)
IP Addresses describe two things - Network section & Host section
  Network section: is like the name of a street
  Host section: is like the house number
Examples:
  192.168.0.1
    192.168.0.1 – Network section, 192.168.0.1 – Host section
  131.107.1.4
    131.107.1.4 – Network section, 131.107.1.4 – Host section
  10.34.2.1
    10.34.2.1 – Network section, 10.34.2.1 – Host section
Subnet Mask
  Shows which section is the network and which is the host

## Slide 11: Subnet Mask
Determines which part of the IP address is the:
  Network section
  Host section
Helps to determine if a destination host is on:
  Local subnet
  Remote subnet
Traditional Class Subnet masks
  Dotted Decimal Binary CIDR
  Class A = 255.0.0.0 = 11111111 00000000 00000000 00000000 = /8
  Class B = 255.255.0.0 = 11111111 11111111 00000000 00000000 = /16
  Class C = 255.255.255.0 = 11111111 11111111 11111111 00000000 = /24
  Class D = no subnet mask specified (Used for multicast)
Traditional masks wasted a lot of address
  Solution = Classless inter-domain routing (CIDR)
  CIDR allows for bitwise manipulation of the subnet mask

## Slide 12: Original IP Classes (assignable addresses)
Class A
  First octet 1-126 (Binary 00000000 – 01111111) [0 & 127 by convention are not used)
  First octet is the network section
  Last three octets are the Host section
Class B
  First octet 128-191 (Binary 10000000 – 10111111)
  First two octets are the network section
  Last two octets are the Host section
Class C
  First octet 192-223 (Binary 11000000 – 11011111)
  First three octets are the network section
  Last octet is the Host section

## Slide 13: ARP – Address Resolution Protocol
ARP resolves an IP address into its corresponding MAC address
ARP request is sent as a broadcast packet
Asks who owns an IP address
  IP owner answers with its MAC address with a unicast packet
  ARP resolution information is cached in memory (for both the sender and receiver)
  ARP cache entries last about 10 minutes in memory
Routers do not pass broadcasts
  Cannot ARP for an IP on a remote subnet
  To communicate with a remote host, route packet through a router
  Set Default Gateway IP so hosts can be used to find the default router
Use arp -a to show the contents of the ARP cache
Use arp -d to delete the contents of the ARP Cache

## Slide 14: ARP in action (Host A to Host D)
01A5431132AB
???
131.107.0.4
131.107.0.7
49791
80
DATA
Ports
IP Addresses
MAC Addresses
Dst
Src
(A) 131.107.0.4/16
(B) 131.107.0.6/16
(C) 131.107.0.3/16
(D) 131.107.0.7/16
01A5431132AB
01A54311ED14
Arp Request
131.107.0.4 -> 01A5431132AB
131.107.0.7 -> ???
Arp Response
131.107.0.7 -> 01A54311ED14
131.107.0.4 -> 01A5431132AB
01A5431132AB
01A54311ED14
131.107.0.4
131.107.0.7
49791
80
DATA
Ports
MAC Addresses
Dst
Src
IP Addresses
Broadcast ARP request to all hosts
Unicast ARP reply to sender
Don’t know remote machine’s MAC Address?
Fill in the MAC Address received

## Slide 15: Default Gateway
Typically set on each host
  Allows the host to route traffic out of the local subnet
  Points to the default router
  Is used when the host needs to:
    Send traffic to a remote network
    There is no specific route for the intended destination
Only used for remote destinations
Sender sends an ARP request for the Default Gateway’s IP address
Sender receives the MAC address of the router’s NIC

## Slide 16: Determine if destination is local or remote
Sending host
  ANDs its IP address with the senders Subnet Mask
  ANDs the destination IP address with the senders Subnet Mask
Compare the results of the previous ANDing calculations
  if the results are the same then the destination IP is local (Computers A & B)
  if the results are different then destination IP is remote (Computers B & C)
A
B
C
D

## Slide 17: Determine how to route traffic
Each time a network transmission happens
  Sender need to determine if destination is on the local or remote network
If the destination IP address is on the local network
  ARP for the destination IP address
  This informs the sender of the remote host’s MAC address
  Send the network packet to the MAC address of the destination host
If the destination IP address is on a remote network
  ARP for the IP address of the Default Gateway
  This informs the sender of the default gateway’s MAC address
  Send the network packet to the MAC address of the default router

## Slide 18: Boolean AND calculation
BOOLEAN AND |  |  |  | 
0 | AND | 0 | = | 0
0 | AND | 1 | = | 0
1 | AND | 0 | = | 0
1 | AND | 1 | = | 1

## Slide 19: Determining if hosts are local or remote
A -> B (Local)
  131.107.0.4 AND 255.255.0.0 = 131.107.0.0
  131.107.0.6 AND 255.255.0.0 = 131.107.0.0
B -> C (Remote)
  131.107.0.6 AND 255.255.0.0 = 131.107.0.0
  131.109.0.3 AND 255.255.0.0 = 131.109.0.0
(A) 131.107.0.4/16
(B) 131.107.0.6/16
(C) 131.109.0.3/16
(D) 131.109.0.7/16
(RG) 131.107.0.1/16
(RR) 131.109.0.1/16

## Slide 20: AND calculation (A -> B)
131.107.0.4 AND 255.255.0.0
  10000011 01101011 00000000 00000100 (131.107.0.4)
  11111111 11111111 00000000 00000000 (255.255.0.0)
  10000011 01101011 00000000 00000000 (131.107.0.0 - AND Result)
131.107.0.6 AND 255.255.0.0
  10000011 01101011 00000000 00000110 (131.107.0.6)
  11111111 11111111 00000000 00000000 (255.255.0.0)
  10000011 01101011 00000000 00000000 (131.107.0.0 - AND Result)
Results are the same – this means the two addresses are local

## Slide 21: AND calculation (B -> C)
131.107.0.6 AND 255.255.0.0
  10000011 01101011 00000000 00000110 (131.107.0.6)
  11111111 11111111 00000000 00000000 (255.255.0.0)
  10000011 01101011 00000000 00000000 (131.107.0.0 - AND Result)
131.109.0.3 AND 255.255.0.0
  10000011 01101101 00000000 00000011 (131.109.0.3)
  11111111 11111111 00000000 00000000 (255.255.0.0)
  10000011 01101101 00000000 00000000 (131.109.0.0 - AND Result)
Results are different
  this means the two addresses are not on the same subnet

## Slide 22: ARP Requests
A -> B (Local)
  From A, ARP for destination IP B
  Reply with MAC address from B
B -> C (Remote)
  From B, ARP for the router RG IP address
  Reply with MAC address from RG
  Send the network packet to the routers MAC address
  From Router, ARP for destination C IP address
  Reply with MAC address from C
(A) 131.107.0.4/16
(B) 131.107.0.6/16
(C) 131.109.0.3/16
(D) 131.109.0.7/16
(RG) 131.107.0.1/16
(RR) 131.109.0.1/16
ARP IP B
ARP IP RG
ARP IP C
MAC B
MAC RG
MAC C

## Slide 23: Routing local (A -> B [Webserver])
(A) 131.107.0.4/16
(B) 131.107.0.6/16
(C) 131.109.0.3/16
(D) 131.109.0.7/16
(RG) 131.107.0.1/16
(RR) 131.109.0.1/16
A
A
MAC
IP
SRC
DST
B
B
50331
80
Port

## Slide 24: Routing remote (B -> C [Webserver])
(A) 131.107.0.4/16
(B) 131.107.0.6/16 Def GW: 131.107.0.1
(C) 131.109.0.3/16 Def GW: 131.109.0.1
(D) 131.109.0.7/16
(RG) 131.107.0.1/16
(RR) 131.109.0.1/16
B
B
MAC
IP
SRC
DST
RG
C
49791
80
Port
Port
RR
B
MAC
IP
SRC
DST
C
C
49791
80

## Slide 25: Routing and NAT (B -> C [Webserver])
(A) 192.168.0.4/16
(B) 192.168.0.6/16 Def GW: 192.168.0.1
(C) 131.109.0.3/16
Def GW: 131.109.0.1
(D) 131.109.0.7/16
(RG) 192.168.0.1/16
(RR) 131.109.0.1/16
B
B
MAC
IP
SRC
DST
RG
C
49961
80
Port
Port
RR
RR
MAC
IP
SRC
DST
C
C
10001
80
192.168.0.6:49961 ---> 131.109.0.1:10001
NAT TABLE
NAT

## Slide 26: Subnetting Introduction

## Slide 27: Why do we subnet
To convert a single network into smaller networks
To reduce wasting of IP addresses
To control network traffic congestion
To manage the growth of a network
To make network security more granular

## Slide 28: How do we subnet
You need to answer several questions before you are ready to subnet
  What network address are we starting with
  How many smaller networks do we need (Subnets)
  How many IP addresses do we need on each subnet (minimum: 1 per NIC)
  What growth do we expect to happen within the subnets
  Is it possible to achieve the result with the given conditions

## Slide 29: What network are we starting with
Class A, B, C each have default subnet masks /8, /16, /24
Some IP addresses on each network have special purposes
We will use 131.12.0.0/16 as an example:
  Network ID: 131.12.0.0/16
  Broadcast ID: 131.12.255.255/16
  The first address in each subnet is its Network ID
  The last address in each subnet is its Broadcast ID
  The Network ID and Broadcast ID are not used for addressing hosts
  So, the usable (valid) addresses are: 131.12.0.1 -> 131.12.255.254 / 16

## Slide 30: Subnetting example - 131.12.0.0/16
Responses from an organisation to our questions:
How many subnets are required
  28
How many IP addresses are required per subnet
  1300
What growth do we expect on these subnets
  5% growth in the number of subnets
  10% growth in IP addresses
Therefore, max subnets: 28 + 5% = 28 + 1.4 (~ 2) = 30
Therefore, max IP addresses: 1300 + 10% = 1300 + 130 = 1430

## Slide 31: Example continued - Calculate subnets
Subnets Required: 30
IP addresses / subnet required : 1430
Starting Network ID: 131.12.0.0/16
/16 means
  That the first 16 bits are network
  This leaves the last 16 bits for us to slice up into smaller subnets
How many bits are required to make at least 30 subnets
5 Bits
  00000 -> 11111 = is 32 possible numbers (we need 30)
That leaves eleven bits for hosts (16 – 5)
  00000000000 -> 11111111111 = 2048 possible numbers – 2 (one for Net ID and one for BC ID)
  2046 IP addresses on each of the 32 subnets
The subnetting is possible!

## Slide 32: How is the subnetting performed
The new subnet mask is the old mask + the network bits required
  Old mask = 16 bits
  Subnet bits required for subnetting = 5 bits
  New subnetting mask = 21 bits
Old 131.12.0.0/16 in binary looks like this:
  10000011 00001100 00000000 00000000
  11111111 11111111 00000000 00000000 (16 bits)
New 131.12.0.0/21 in binary looks like this:
  10000011 00001100 00000000 00000000 (Subnet portion Host portion)
  11111111 11111111 11111000 00000000 (21 bits)

## Slide 33: How to create the first subnet
10000011 00001100 00000000 00000000
The first subnet would look like this in binary:
  10000011 00001100 00000000 00000000 - Subnet ID
  10000011 00001100 00000000 00000001 - First valid address
  10000011 00001100 00000111 11111110 - Last valid address
  10000011 00001100 00000111 11111111 - Broadcast ID
In Decimal
  131.12.0.0 - Subnet ID
  131.12.0.1 - First valid address
  131.12.7.254 - Last valid address
  131.12.7.255 - Broadcast ID

## Slide 34: How to create the second subnet
10000011 00001100 00001000 00000000
The second subnet would look like this in binary:
  10000011 00001100 00001000 00000000 - Subnet ID
  10000011 00001100 00001000 00000001 - First valid address
  10000011 00001100 00001111 11111110 - Last valid address
  10000011 00001100 00001111 11111111 - Broadcast ID
In Decimal
  131.12.8.0 - Subnet ID
  131.12.8.1 - First valid address
  131.12.15.254 - Last valid address
  131.12.15.255 - Broadcast ID

## Slide 35: How to create the third subnet
10000011 00001100 00010000 00000000
The third subnet would look like this in binary:
  10000011 00001100 00010000 00000000 - Subnet ID
  10000011 00001100 00010000 00000001 - First valid address
  10000011 00001100 00010111 11111110 - Last valid address
  10000011 00001100 00010111 11111111 - Broadcast ID
In Decimal
  131.12.16.0 - Subnet ID
  131.12.16.1 - First valid address
  131.12.23.254 - Last valid address
  131.12.23.255 - Broadcast ID

## Slide 36: How to create the fourth subnet
10000011 00001100 00011000 00000000
The fourth subnet would look like this in binary:
  10000011 00001100 00011000 00000000 - Subnet ID
  10000011 00001100 00011000 00000001 - First valid address
  10000011 00001100 00011111 11111110 - Last valid address
  10000011 00001100 00011111 11111111 - Broadcast ID
In Decimal
  131.12.24.0 - Subnet ID
  131.12.24.1 - First valid address
  131.12.31.254 - Last valid address
  131.12.31.255 - Broadcast ID

## Slide 37: Supernetting Introduction

## Slide 38: Why Supernetting
Optimising Route tables
Creating larger networks by combining networks
It is the opposite to subnetting

## Slide 39: How to Supernet
Combined networks are only in sets of 2,4,8,16,32 …
Supernetting only can combine subsequent networks together
The binary bits that are being swapped from subnet to host must:
  Start with all binary 0’s
  End with all binary 1’s

## Slide 40: Supernet Example
Situation:
  Need 1000 hosts on a single network
  Class C networks are all we have to work with
  Each class C network only gives us 256 - 2 = 254 host addresses
What is required
  Determine the number of bits to accommodate 1000 hosts?
    Ten bits minimum are required to provide 1000 hosts
    Using groups of class C we would need 4 subnets (1024 - 2 = 1022 hosts)

## Slide 41: Supernet Solution
Using these 4 networks
  191.9.8.0/24, 191.9.9.0/24, 191.9.10.0/24, 191.9.11.0/24
10111111 00001001 00001000 00000000 /24
10111111 00001001 00001001 00000000 /24
10111111 00001001 00001010 00000000 /24
10111111 00001001 00001011 00000000 /24
------------------------------------------------------------
10111111 00001001 00001000 00000000 /22
191.9.8.0/22 [1 subnet, 1022 hosts (1024 - 2) ]
Bits 23 and 24 start at 00 and end with 11 this
is a requirement
By removing bits 23 and 24 from the subnet mask we create 1 subnet from 4 subnets

## Slide 42: Variable Length Subnet Masks (VLSM)

## Slide 43: Why VLSM
The subnets we need are rarely the same size
We need some subnets that only require two host addresses (WANs)
VLSM is a more efficient use of network address space
It is much more practical to use VLSM

## Slide 44: VLSM Example
1st network requires 100 hosts (Sydney)
2nd network requires 20 hosts (Philippines)
3rd network requires 15 hosts (Perth)
4th network is a WAN links that require 2 hosts (Per -> Syd)
5th network is a WAN links that require 2 hosts (Syd -> Php)
Network to subnet is 189.10.10.0/24
Perth
Sydney
Philippines
WAN
WAN

## Slide 45: VLSM Box method
198.10.10.
0
255
/24

## Slide 46: VLSM Box method
198.10.10.
0
255
/25
/25
127
128

## Slide 47: VLSM Box method
198.10.10.
0
255
/25
/25
127
128
SYDNEY

## Slide 48: VLSM Box method
198.10.10.
0
255
/26
/25
127
128
/26
192
191
SYDNEY

## Slide 49: VLSM Box method
198.10.10.
0
255
/25
127
128
/27
192
191
/27
160
159
SYDNEY
/26

## Slide 50: VLSM Box method
198.10.10.
0
255
/25
127
128
/27
192
191
/27
160
159
SYDNEY
/26
PHILIPPINES
PERTH

## Slide 51: VLSM Box method
198.10.10.
0
255
/25
127
128
/27
192
191
/27
160
159
SYDNEY
/27
/27
224
223
PHILIPPINES
PERTH

## Slide 52: VLSM Box method
198.10.10.
0
255
/25
127
128
/27
192
191
/27
160
159
SYDNEY
PHILIPPINES
PERTH
/27
/28
224
223
/28
240
239

## Slide 53: VLSM Box method
198.10.10.
0
255
/25
127
128
/27
192
191
/27
160
159
SYDNEY
PHILIPPINES
PERTH
/27
/29
224
223
/28
240
239
/29
248
247

## Slide 54: VLSM Box method
198.10.10.
0
255
/25
127
128
/27
191
/27
160
159
SYDNEY
PHILIPPINES
PERTH
/30
248
252
251
/30
192
/27
223
224
/28
239
/29
240
247

## Slide 55: VLSM Box method
198.10.10.
0
255
/25
127
128
/27
191
/27
160
159
SYDNEY
PHILIPPINES
PERTH
/30 - WAN
248
252
251
/30 - WAN
192
/27
223
224
/28
239
/29
240
247

## Slide 56: VLSM Box method
198.10.10.
0
255
/25
127
128
/27
191
/27
160
159
SYDNEY
PHILIPPINES
PERTH
/30 - WAN
248
252
251
/30 - WAN
192
/27
223
224
/28
239
/29
240
247
SPARE SUBNETS

## Slide 57: VLSM Solution
Sydney
  198.10.10.0/25 (198.10.10.1 - 198.10.10.126) [100/126 hosts]
Philippines
  198.10.10.128/27 (198.10.10.129 - 198.10.10.158) [20/30 hosts]
Perth
  198.10.10.160/27 (198.10.10.161 - 198.10.10.190) [15/30 hosts]
WAN
  198.10.10.248/30 (198.10.10.249 - 198.10.10.250) [2/2 hosts]
WAN
  198.10.10.252/30 (198.10.10.253 - 198.10.10.254) [2/2 hosts]
Spare
  Three subnets spare for future network growth